## Slide 1
resilient Communications Middleware for IoT Data Exchange
Kyle E. Benson
University of California, Irvine
Under advisement of Nalini Venkatasubramanian

## Slide 2: Dissertation Outline
Background
Proposed Middleware
Geo-aware overlays for cloud data collection
IoT Data Exchange
Our Experiences
Motivating Resilience Challenges in mission-critical scenarios
Edge fail-over and local alerting
Information prioritization to address resource constraints
Network & application-awareness, SDN & edge computing
Notes: 1) improve cloud collection
2) ensures downtime of no more than...
3) improves edge alert delivery by....
4) firedex conclusion

## Slide 3: IoT Data Exchange
Physical Events
& Actions
Communications
Networks
Cloud Services
User
Applications
Devices
Spaces
Data
Exchange
Constrained
devices!
We assume a topic-based pub/sub model

## Slide 4
Analytics / Alerting Cloud
Dispatch Center
First responders arrive
Long-range wireless antenna
Yes!
Emergency?
Resident / Caretaker
Resident in distress
SCALE sends emergency message
“Democratizing safety by bringing the Internet of Things (IoT) to everyone”
Notes: Inspired by IoT-enhanced emergency response possibilities, we explored the use of off-the-shelf IoT hardware in creating a smart safe home / community environment.
Multi-sector team of organizations demonstrating IoT for community safety in response to 2013 White House/NIST SmartAmerica Challenge
I led development on SCALE as an Innovation Fellow in Montgomery County, MD in Spring 2014. Many thanks to other primary devs Guoxi and Qiuxi.
[WORKFLOW OVERVIEW]
SCALE has since expanded to include many more partners and served as a testbed for various research projects in our group.

## Slide 5: SCALE’s heterogeneous evolution
SCALE expanded and used as a test-bed in many projects:
Benson et al. “SCALE: Safe Community Awareness and Alerting Leveraging the Internet of Things”. IEEE Communications, December 2015.
Uddin et al. “The SCALE2 Multi-network Architecture for IoT-based Resilient Communities”. SMARTCOMP ’16.
Benson et al. “Resilient Overlays for IoT-based Community Infrastructure Communications”. IoTDI ’16
Zhu et al. “Upload Planning for Mobile Data Collection in Smart Community Internet-of-Things Deployments”. SMARTCOMP ‘16.
Mehrotra et al. "TIPPERS: A Privacy Cognizant IoT Environment". in First IEEE International Workshop on Security, Privacy and Trust for IoT, Sydney, Australia. 2016.
Han et al. "Toward An Integrated Approach to Localizing Failures in Community Water Networks". ICDCS ’17.
Nailah Alhassoun, Md Yusuf Sarwar Uddin, and Nalini Venkatasubramanian. “SAFER: An IoT-Based Perpetual Safe Community Awareness and Alerting Network”. IGSC ’17.
Zhu et al. "Data Collection and Upload under Dynamicity in Smart Community Internet-of-Things Deployments". Pervasive and Mobile Computing (2017).
Hera et al. "Adaptive Sensing Using Internet-of-Things with Constrained Communications". Workshop on Adaptive and Reflective Middleware (ARM), co-located with ACM/IFIP/USENIX Middleware, 2017.
Benson et al. “Ride: A Resilient IoT Data Exchange Middleware Leveraging SDN and Edge Cloud Resources”. IoTDI ‘18.
Benson et al. "FireDeX: a Prioritized IoT Data Exchange Middleware for Emergency Response". (to appear in) Middleware ’18.
Zhu et al. "Spatiotemporal Scheduling for Crowd Augmented Urban Sensing". INFOCOM ‘18.
… and hopefully many more!
Notes: --------
Found the cloud-centric DX very flexible and easy to add new features, but still non-trivial to maintain connections

## Slide 6: IoT Data Exchange
/events/fire/location?room=dsm_lab
any.smoke.sensors.dbh.uci.edu
GET coap://
?
Physical Events
& Actions
Communications
Networks
User
Applications
Devices &
Infrastructure
Data
Exchange
Notes: TODO:
TODO: maybe show a step of abstracting smoke sensors into just ‘observe fire’
TODO: need to get across subscribe/publish idea here… maybe use icons to show another workflow here? E.g. querying for smoke alarms to detect a fire vs. observe a fire event that another service creates by observing the smoke events: DX!
-------
Semantic gap!
separates concerns de-coupling devices and users, locations, even time (observe)
-------

## Slide 7: Mission-Critical IoT Scenario: Earthquake Safety
Notes: Alert impacted people and query if okay (didja feel it?)
Activate infrastructure: Stop elevators, (sirens, flashing lights for the deaf)
monitor environment: fires, gas leaks

## Slide 8: IoT Data Exchange Resilience
We identified this challenge during SCALE in 2014…
Ensuring operation despite challenging conditions e.g. failures.
Physical Events
& Actions
Communications
Networks
Cloud Services
User
Applications
Devices
Spaces
Data
Exchange
?
?
?
?
?
?

## Slide 9: Edge Computing for IoT DX Resilience
Ride leverages resources at the network edge for:
Resilience to cloud disruptions e.g. edge fail-over in response to wide-area network failures
Decreased latency
Localized operation e.g. local situational awareness generation
Communications
Networks
Cloud Services
User
Applications
IoT Devices
Data
Exchange
…
…
Diverse networking for resilience (i.e. different routes and physical networks).
Software-defined networking (SDN) enables more flexible management of these diverse networks!
Edge Infrastructure
Notes: -------
SPEECH
Edge computing is frequently discussed in the context of 5G, whose architecture allows running services nearer to the base stations for…
Different network routes, which may or may not mean entirely different physical network technologies.
------

## Slide 10: Software-Defined Networking (SDN)
virtual net abstraction
VPN, QoS, security
SDN Controllers
Virtual
Switches
Physical
Switches
unified APIs
Control Plane
Data Plane
Net. Services
Global Network State
Local IoT Controller
Proposed Middleware
…
…
…
Various APIs
source: Dungay 2016
physical infrastructure
Application workflows
Like Zhang 2013’s “big idea” paper proposed SDN-like logically-centralized control of pub/sub in combination with SDN.
Our proposal improves network-awareness, control, and resilience.
Notes: -----
SPEECH:
Control vs. data plane… centralization
SDN lets us manage physical network infrastructure with the same abstractions / APIs used for managing virtual networks of cloud services…
Centrally viewing network state to optimize the whole IoT communications network from the SDN controllers, where we…
deploy network services such as those in our proposed m/w to centrally manage IoT networking along with IoT data exchange and application workflows…
sounds familiar? SDN-like
-------

## Slide 11: Proposed Approach
Middleware extends existing IoT Data Exchange solutions for enhanced resilience.
Leverages application and network awareness.
Configures physical infrastructure through programmable network APIs / abstractions.
Edge intelligence mitigates cloud / network disruptions.
Applications
Data Exchange
Middleware
Physical
Infrastructure
Users
Personal safety &
alerting
Programmable
Networks
State
Aware
Dev
Net
Interactions
App
Network
Comms. Adaptation
IoT Data Exchange
protocols, brokers, algorithms, etc.
Devices
semantic notifications
actuation responses
Seismic response& early warning
Smart Fire Fighting
response
…
sensed events
commands
requirements
edge
cloud
Notes: -------
SPEECH
To support mission-critical apps, they share resilience requirements
M/W gathers infrastructure info using programmable networks
Bridging network and data exchange
QUESTION: How do we bridge network and data exchange?

## Slide 12: Comparing the 3 Core Chapters
GeoCRON
Ride
FireDeX
Cloud-centric data collection
Cloud vs. edge & local alerting
Satisfy information requirements
Information value and resource constraints (B/W)
App. requirements, local topology, connectivity info.
Device & router topology + node locations
Data exchange goals
Approach to resilience
Earthquake-detection
Local seismic early-warning
Smart fire fighting response
State information
Failure avoidance (geo-redundancy)
Failure recovery (edge fail-over)
Resource allocation (prioritize data)
Validation setting
“Ride: A Resilient IoT Data Exchange Middleware Leveraging SDN and Edge Cloud Resources”. IoTDI ‘18.
(Thanks Guoxi!)
“Resilient Overlays for IoT-based Community Infrastructure Communications”. IoTDI ’16
Earlier work in PerNEM ’13 workshop.
(Thanks Qing and Kyungbaek!)
"FireDeX: a Prioritized IoT Data Exchange Middleware for Emergency Response". Middleware ’18.
(Thanks Georgios & Luca!)
Notes: --------
SPEECH
1: more edge as we evolve (IoT devs vs. edge infra vs. BMS)
2: reactive vs. proactive vs. supporting dynamics
3: progressively more semantic / high-level
4: increasing complexity of scenarios
-------
MAYBE: outline version with another row:
Community-scale geo-aware overlays
Campus-scale SDN infrastructure control
Building-scale SDN data flow management

## Slide 13
GeoCRON
- Community-scale wide-area IoT network
- Geo-aware cloud overlays
Ride
- Smart campus network
- SDN control over (local) edge infrastructure and cloud overlays
FireDeX
- Building-area
network
- SDN for data flows
Network abstractions used in each chapter
SDN
“big switch”
SDN “big switch” abstracts underlying network e.g. physical link, overlay, GeoCRON , Ride etc.
Cloud data path overlays could be created using GeoCRON.
Notes: -------
SPEECH
more edge as we evolve (IoT devs vs. edge infra vs. BMS)
SDN abstractions each level down build on/incorporate the one above

## Slide 14: Proposed Middleware Architecture
IoT Devices
IoT DX Middleware
Geo-diverse multi-path
Routing (GeoCRON)
Building Management System Interface
Seismic “pick”
Resilient Overlay Networks
Cloud Services
Analytics
Edge Services
Backup analytics
Resilient alert
Producers
Prioritized subscription
Ride
data collection
Differen-tiated info flow
Local Data Exchange
IoT data
Consumers
Resilient alert subscription
FireDeX
BW Allocation
Prioritization
Ride
Diverse multicast
Is
cloud
up?
Yes
No
SDN
Ride overlay probe

## Slide 15: Publications, Posters, & Presentations…
Ride
GeoCRON
Smart fire
fighting
SCALE
GeoCRON
(early)
Shanty
town fire
Undergrad research
(seismic sensing
simulations)
SmartGrid
resilience
"FireDeX: a Prioritized IoT Data Exchange Middleware for Emergency Response". to appear in Middleware ’18.

## Slide 16
Source: csn.caltech.edu
Many thanks to CSN!
Low-cost accelerometers attached to IoT computers measure shaking and report anomalies…
Cloud-based machine learning algorithms detect earthquakes.
CSN produces fine-grained shake maps that can aid emergency response efforts.
We added CSN’s sensors to SCALE.
How to resiliently collect data in the cloud despite wide-area network failures?
Notes: -----------
SPEECH
Overview CSN…
Gave us sensors; we added to SCALE Box, which is modeled after CSN’s deployment.
QCN asked my undergrad team to simulate expected detection during a quake…. We got to thinking about failures then but now we’re really trying to address
Thought on way back from csn meeting…
Use CSN devices as overlay nodes to route around failures?
----------

## Slide 17: GeoCRON: Geo-correlated failure-aware Resilient Overlay Networks for IoT-based Community Infrastructure Communications
Seismic Sensors
Water
Sensors
Cloud earthquake-detection service
seismic sensed events
Fine-grained shake map
P(d1)
P(d2)
d1
d2
Applications
Data Exchange
Middleware
Physical Infrastructure
IoT Peers
Fail-
ures
Overlay Path Configurations
GeoCRON
Control
Algorithm
Topo
seismic data
P’(d1)
Notes: -------
Because CSN is a planned deployment (owns/manages devices), Geocron proposes leveraging edge intelligence of IoT devices
Geo-Resilient routing sort of like p2p overlay except centrally controlled and any-to-one rather than any-to-any
Peers + topology + seismic failure model (and locations of these) = overlay paths
d1’s normal path P(d1) to the cloud may fail during the pictured earthquake.

## Slide 18
Earthquake-
Inspired
Failure
Model & Simulations
ns-3 simulations using router topologies from:
  Rocketfuel – actual country-scale AS topology estimates connecting distant cities (Spring 02)
  BRITE - random router-level AS topology generator (Medina 01)
  Our (Benson 13) community-scale IoT infrastructure topology
    Based on real water distribution network and population estimates.
    Generated with I-Gen
    (Quoitin 09)
Notes: -------
SPEECH
Studied GeoCRON using a network simulator to which we added an earthquake-inspired failure model over various network topologies
  Country-scale (USA) real-world estimations vs. randomly-generated AS’s vs. a more detailed smart city/ community-scale topology (based on real water distribution network that we used to estimate population densities, place IoT sensors, and construct a physical routing topology for)
  ----------
BACKUP NOTES:
TOPOLOGY: North Marin County, Novato, CA (~27 routers + ~270 sensors)

## Slide 19: Heuristics for Constructing Multiple Geo-diverse Paths
Uniform random (baseline)
“Ideal” oracle heuristic
Weighted combination of: (Rohrer 2014)
  Min. distance between any two pairs of nodes
  chosen from the two paths
  Area of polygon formed by paths as borders
Penalty for each proximal component
(routers or links) along paths
  Gs-Ford: proximal = within distance threshold (Kim 2010)
  Intersection: proximal = same exact component (Rohrer 2014)
Our first investigations (Benson 2013) considered
device locations only (no topology knowledge)
  Explored different distances between nodes (near vs. far), regions (breaking into a grid), and angles (similar to Rohrer 2013’s area heuristic)
  However, we determined these heuristics were all
  inferior to those with actual topology knowledge
Source: Rohrer 2013
Source: Cheng 2014

## Slide 20: Simulation Results - Heuristics
Awareness about the underlying physical topology improves data collection!

## Slide 21: Simulation Results – # Disjoint Paths
Diminishing returns for > 5 disjoint paths
This agrees with (Rohrer 2014) results: most topologies only show strong increases for k<7
Notes: Diminishing returns after k=5
However, it delivers data quicker! This may be advantageous for real-time alerting…

## Slide 22: Simulation Results – Failure Rate
Too many failures severely hampers data collection.
Cannot reach cloud…
But maybe the edge?
Notes: very high failures make cloud nearly unreachable…. Maybe edge?

## Slide 23: GeoCRON extra
Notes: Show topo overlaid on these maps
Why didn’t we do this? Security/Privacy concerns for volunteers

## Slide 24: Proposed Middleware Architecture
IoT Devices
IoT DX Middleware
Geo-diverse multi-path
Routing (GeoCRON)
Seismic “pick”
Resilient Overlay Networks
Cloud Services
Analytics
Edge Services
Backup analytics
Resilient alert
Producers
Ride
data collection
Local Data Exchange
Consumers
Resilient alert subscription
Ride
Diverse multicast
Is
cloud
up?
Yes
No
SDN
Ride overlay probe
What if cloud is unavailable?
Fail over to the edge!
How to improve local alerting?

## Slide 25: Ride: A Resilient IoT Data Exchange Middleware Leveraging SDN and Edge Cloud Resources
Applications
Ride-C
resilient IoT data collection
Cloud
service
monit-
oring
State Awareness
adapt net.
App
Net
Edge
fail-over
Data Exchange
Middleware
Physical
Infrastructure
SDN
Ride-D
resilient alert dissemination
Users
alerts
sensed events
Smart (IoT) Community Safety Apps
situational awareness
app reqs.
Problem: regional infra. failures/ cloud service disruptions
  Viewed from local (campus/community) perspective.
  The organization controls local infrastructure and deploys IoT devices there…
Proposed solution: leverage local edge resources when needed
  I.e. during cloud service disruptions.
  SDN facilitates local network infrastructure awareness & control.
  Ride captures app requirements.
alerts
Notes: ------
SPEECH
Treat app logic as a black box
Awareness… enables Ride to be both application and network aware
Ride-C generates network awareness as a by-product of its local data collection when in edge mode!
------------

## Slide 26: Ride Research Questions
Ride-C
How to ensure cloud service stability or edge fail-over according to application-specified resilience requirements?
Without over-burdening constrained IoT devices or edge network infrastructure?
Ride-D
How to leverage network awareness for more resilient local alerting?
Without over-burdening constrained IoT devices or edge network infrastructure?

## Slide 27: Ride-C: Resilient Data Collection
Path Purpose | Line
Data Collection | 
Probing | 
Failover | 
Setting Up Data Collection Routes
Adaptive Probing and Failover
Cloud Alerting Server
Edge Alerting Server

## Slide 28: Ride-C Algorithm
  Monitors multiple Cloud Overlay Paths for resilient data collection.
  Adaptation Process:
    Number of Probes for Detection
      Maximum False Positive Rate, Link Loss Rate
    Probe Interval:
      Number of Probes for Detection, Maximum Detection Time
Network State
App Requirements
Adaptive Probing
Max. Detection Time
Max. False Positive Rate
Average Round-trip Time
Path Loss Rate
Probing Interval
Failure Detection Parameters
    Conserves resources e.g. bandwidth.
    Meets detection
    time requirement.
Notes: OUTPUT PARAMS: # Probes that timed out after a period

## Slide 29
  Monitors DataPaths to the cloud.
  Adaptive probing adjusts interval:
    Conserves resources e.g. bandwidth.
    Meets detection time requirement.
Ride-C Algorithms

## Slide 30: Ride-D: Resilient Alert Dissemination
Edge Alerting Service
sensor2
sensor1
sensor3
Data Collection path (Ride-C) | 
MDMT 1 | 
MDMT 2 | 
MDMT 1 & 2 | 
Maximally-Disjoint Multicast Trees*
|T1 ^ STT| < |T2 ^ STT|
Successfully-
Traversed
Topology*
*Pre-configured via SDN
(OpenFlow flow rules)
No device burden!
Cloud is down!
Notes: --------
Speech
Operating in edge mode, so local Time critical earthquake warning
Multicast lets us reach relevant subscribers with efficient network bandwidth usage (e.g. rich notifications)
To enhance resilience (i.e. improve reachability despite local failures), we exploit topological diversity by constructing MDMTs…
Multicast path protection is not new… but our technique for selecting the tree at alert-time rather than using one as a primary and one as backup is!
Network-aware tree selection based not on known link status, which takes time for control plane to gather, but on sensor publications recently-received via functional links:
We consider the local sensor data collection paths configured by Ride-C; produce a by-product of that phase: STT
*SDN enables STT
sensor1’s data never delivered, so MDMT 2 “overlaps” with STT more than MDMT 1

## Slide 31: Ride-D Algorithms
MDMT
Construction
Network-aware
MDMT Selection
steiner: bounded low cost appx. (Hwang 1992)
diverse-paths: one subscriber at a time
red-blue: edge-disjoint pair of trees
Iteratively increase weight of used edges
Disjoint paths generated using (Zheng 2010)
Split topology recursively using Bejerano 2013’s skeleton list data structure
Min-cost multicast trees NP-Hard! Heuristics:
max-overlap-links with STT
min-missing-links from STT
max-link-importance: hybrid of others
Sum of STT links’ importance:
# subscriber-paths traversing the link.
STT indicates likely functional paths from Ride-C data paths  heuristics:
max-reachable-subscribers via complete STT paths
Red-blue algorithm
Source: Bejerano 2013
Notes: ---------
SPEECH
Because generating even a single multicast tree of min cost is NP-Hard, we compared several heuristics derived from existing algorithms…
One of our key contributions is the mechanism for selecting MDMTs in a network-aware manner and the following proposed policies:
- some look at the overlap of STT and MDMTs, one the # subscribers reachable via intersection of STT and MDMT, and our best policy combines these two to consider the importance of MDMT links present in STT
------
MAYBE: Pictures: could show the little ‘4 constellations’ diagram on right with big ? Mark
----------
BACKUP notes
Steiner: minimum spanning tree of the metric closure subgraph
Diverse-paths: min-cost network-flow based, start with subscriber closest to server, add paths to MDMT with max overlap to reduce cost
Red-blue: trims links to create mdmt
TODO: runtime complexities!
TODO: explain difference between min-missing and max-overlap

## Slide 32: Ride-D Algorithm Details
min-missing-links
max-overlap-links
max-reachable-subscribers
max-link-importance
Notes: ---------
SPEECH
Because generating even a single multicast tree of min cost is NP-Hard, we compared several heuristics derived from existing algorithms…
One of our key contributions is the mechanism for selecting MDMTs in a network-aware manner and the following proposed policies:
- some look at the overlap of STT and MDMTs, one the # subscribers reachable via intersection of STT and MDMT, and our best policy combines these two to consider the importance of MDMT links present in STT
------
MAYBE: Pictures: could show the little ‘4 constellations’ diagram on right with big ? Mark
----------
BACKUP notes
Steiner: minimum spanning tree of the metric closure subgraph
Diverse-paths: min-cost network-flow based, start with subscriber closest to server, add paths to MDMT with max overlap to reduce cost
Red-blue: trims links to create mdmt
TODO: runtime complexities!
TODO: explain difference between min-missing and max-overlap

## Slide 33: Ride Workflow
Register applications’ resilience requirements and subscriptions. Configure CDP monitoring and MDMTs.
Maintain network state awareness, cloud data paths, and MDMTs.
Adapt to failures via SDN-based CDP/edge fail-over. Gather updated network awareness for resilient local alerting.

## Slide 34: Real-world Test-bed & Experiments
Unplug Ethernet cables
Reconnect Ethernet cables

## Slide 35: Experimental Setup
Generate synthetic campus network topologies
Network failures
(uniformly-random)
Emulate an IP network (via Mininet)
Configure Ride-enabled SCALE clients as:
Event publishers & Alert subscribers
(uniformly random)
Output events  parse & plot results
Notes: Need to talk about Mininet and get across how difficult it was to setup our test-bed environment that other group members will be using

## Slide 36: End-to-end Experiments
Earthquakes trigger seismic data uploads and failures
Cloud path fail-over misses a few secs.
Edge fail-over & local net failures
Cloud path recovery
High data loss/delay during local failure and edge fail-over indicates needed improvements to SDN fail-over mechanism (e.g. partial pre-installation of fail-over routes).
Notes: -----
SPEECH
Scenario includes several different earthquakes each of which …. To showcase different aspects of Ride
The Top bars represents alerting services’ view of received event data
Bottom bars represent alert subsribers’ view of received alert data
(Time placement of quakes not realistic: only for simplicity of demonstration….)

## Slide 37: Ride-C Parameters: Detection Time / Overhead Trade-off
Ride-C meets or exceeds detection time requirement.
If app can tolerate a few seconds of failure detection time, Ride-C can significantly reduce probing overhead.

## Slide 38: Ride-C Comparison with Previous Related Works
* RON FD: Andersen et al. 2001
* B-AFD: Dong et al. 2014
Ride-C detects failures with lower overhead while satisfying detection time requirements.
Notes: -----
SPEECH
We see that the adaptive failure detectors always perform with lower overhead compared with RON

## Slide 39: Ride-D MDMT-Construction
(rate of alert delivery to subscribers)
red-blue
for k<4
diminishing returns 
Correct selection > unicast
worse than unicast due to trees’ fragility!
k=2 : Enyedi 2009-2011 finds 2 maximally-disjoint spanning trees in linear time
(RFC 7811 proposes using this for fast-reroute!)
k=3 : Cheriyan 1988 finds 3 independent spanning trees in 3-connected graphs by inducing cycles
k=4 : Huck 1994 find 4 independent spanning trees in planar 4-connected graphs
Notes: -------
Ride-D large-scale evaluations done in purely simulated setup.
K-connected means: removing k-1 vertices cannot disconnect the graph

## Slide 40: Ride-D MDMT-Selection
(rate of alert delivery to subscribers)
max-link-importance
for k > 2
State-aware heuristics better
Notes: -------
Results shown for red-blue construction, but others appear similar

## Slide 41: Ride-D Overhead Improvement
Ride-D multicast improves overhead
Resilience holds with increasing subscribers
More subscribers  more improvement
Notes: -------
LINK COST: total cost for that MDMT: metric cost for construction algs.

## Slide 42
Conclusions
We demonstrated Ride: a Resilient IoT Data Exchange middleware
  Adapts to cloud disruptions and local failures using SDN and edge resources
  Avoids over-burdening constrained IoT devices
  Practical feasibility study
Ride shows promise; much more to explore!
Future Directions
Ride-C: Data collection
  Improve SDN fail-over time.
  Intelligently split data across multiple cloud data paths.
  Currently-functional topology estimation via dynamic routes using packet tagging (e.g. Gyllstrom 2014)
Ride-D: Alert dissemination
  Adaptively re-transmit by gathering further network state from alert responses (ACKs)
  Integrating P2P-style resilient application-layer multicast to forward alerts between subscribers
Notes: Packet tagging: apply VLAN header at start of a path and count how many make it to end. Jim Kurose! Backup multicast trees
Could easily try out passing to neighbor devices using CoAP observe
  Could look at MQTT “ALM” with CoAP lateral pass

## Slide 43: Proposed Middleware Architecture
IoT Devices
IoT DX Middleware
Geo-diverse multi-path
Routing (GeoCRON)
Building Management System Interface
Seismic “pick”
Resilient Overlay Networks
Cloud Services
Analytics
Edge Services
Backup analytics
Resilient alert
Producers
Prioritized subscription
Ride
data collection
Differen-tiated info flow
Local Data Exchange
IoT data
Consumers
Resilient alert subscription
FireDeX
BW Allocation
Prioritization
Ride
Diverse multicast
Is
cloud
up?
Yes
No
SDN
Ride overlay probe
How to balance needs of multiple emergency apps?
How to handle evolving scenarios & conditions?

## Slide 44: Research Roadmap for Smart Fire Fighting
2015 NIST/NFPA publication that “establishes the scientific and technical basis” of smart fire fighting.
It identified key challenges that motivate our Sci-Fire project.
Collaborative effort involving industry, government, fire science practitioners, and academia.
We co-authored three chapters drawing from our experiences in IoT, CPS, and smart fire fighting.
www.nfpa.org/SmartFireFighting
Notes: Getting the right data to the right people without overloading them
----- Meeting Notes (10/26/18 15:31) -----
add actual references to the 3 chapters!

## Slide 45
IoT-Enhanced Structural Fire Response
Emergency Dispatch
Incident
Command
Post
IoT-enabled Building
Fire fighters & Equipment
Fire Department
How to connect?
Information requirements
FireDeX

## Slide 46: Data Exchange in Smart Fire Fighting
Smart FF fuses sensor data and computing power to drive analytics
  Building management systems (BMS) grant access to data, devices, and infrastructure
  Data exchange fuses with other sources and guides information flow
Goals involve many stakeholders:
  Incident Commander (IC) guides response
  Safety/health of occupants and fire fighters
  Minimize property loss and disruption
Data-driven approach to FF:
  Post-incident forensics e.g. insurance
  Real-time data for situational awareness
Raw data sources
Stakeholders
Analytics
Data
Exchange
Forensics “Black Box”
Incident Commander
BMS
FFs & equip.
Notes: TODO: need to capture CPS angle a bit better… maybe bring a drone or robot in here?
We don’t really show taking actions from the data
TODO: bring hard numbers from research roadmap in to turn “goals”  improvement metrics?

## Slide 47: FireDeX: a Prioritized IoT Data Exchange Middleware for Emergency Response
Pub/Sub Broker
publish <topic>
Event Prioritization
subscribe <topic, utility>
notify <topic>
SDN
“big switch”
notify <subscriber, priority>
subscribe
<topic>
Data Exchange
Middleware
Applications
Network
Infrastructure
Situational Awareness Apps
e.g. FF HUD, IC Dashboard, civilian alerts
situational awareness
Problem: varying information requirements and network conditions as the scenario evolves.
Solution: middleware configures the data exchange & network with prioritization policies based on:
  Information requirements
  Network resource constraints
Approach: queueing theory to model performance and SDN to manage heterogeneous network without broker modifications.
info. reqs.
net. tuning
BMS
Packet Drop Rates
SDN Controller
Unmodified!
Use any impl…
Notes: ------
Info reqs: : event subscriptions with a utility function that captures the value of heterogeneous data collection and determines the priority assigned to events
  Network resources:: available bandwidth, latency, loss rates, etc.  : assign available bandwidth via packet drop rates.
  SDN facilitates awareness of and control over underlying heterogeneous network infrastructure.
“big switch” abstracts the underlying physical network.
  DX views network connections through multiple routes and different technologies as a single programmable SDN switch that exposes aggregate state characteristics of the underlying network.
  This abstraction can incorporate e.g. geo-aware overlays, resilient multicast data delivery, edge fail-over routes, etc.

## Slide 48: Mapping Info. Reqs. to Network Layer
App / DX concept
Network concepts
FireDeX configurations
Topics
Notes: Differentiating messages for different subscriptions

## Slide 49: Modeling FireDeX using Queuing Theory
Queuing network model enables analysis & config.
Data exchange-layer queues represent distributed pub/sub.
Network-layer queues capture bandwidth constraints, error rates, latency, etc.
Only subscribers’ network configured.
Qout is a new queueing model we derived (thanks Ioannis).
delivery rate and end-to-end delay of events for each subscription rj
Enforcing drop rates
Topics mapped to many possible subscriptions
Enforcing priority queueing discipline
Notes: ------
Queue models allow us to “plug-and-play” different models to account for different scenarios:
  On/Off queues for IoT device intermittent connectivity
  Buffer size constraints
  Reliable vs. best-effort transmission
Data exchange broker model
  In queue compares publications to subscriptions, dropping unmatched and forwarding matched ones to subscriber queues and other brokers
  Subscriber queues forward events to that subscriber’s SDN switch.
SDN big switch model
  Every subscriber connects with one switch; shared channels captured by multiple subscribers on the same switch.
  Priority queue forwards most important data first to…
  …the multi-class queue captures bandwidth constraints and transmission delays

## Slide 50: Prioritization Algorithm
Sort subscriptions by information value per unit of bandwidth.
Group them into approximately equal-sized network flows.
  Enables SDN network layer to differentiate subscriptions
  (e.g. by UDP/TCP port number + IP addr).
  Represents network connections for different apps, subs. within app…
Priorities assigned to approximately equal-sized groups of network flows.
Maximum utility achievable for subscription rj
Serialized packet size for topic vj notifications
Rate of notifications (publications) for subscription rj

## Slide 51: Drop Rate Algorithm
Formulated as a convex optimization problem.
  Maximize overall utility as sum of all subscriptions’ utilities.
  Enabled by choice of logarithm for utility function.
  Akin to Network Utility Max.
2nd constraint: queue stability condition
  Ensures allocated bandwidth within that available
  For each SDN switch queue
Utility captured by subscription rj
Success rate of notifications for subscription rj
Utility weight for subscription rj
Drop rates for each network flow
“Rho tolerance” enables keeping a buffer within the bandwidth (~0.1)

## Slide 52: Prototype Implementation

## Slide 53: Experimental Setup
*(7 flows/prios with prototype)*
Notes: Two event types
Random variable distributions

## Slide 54: Model Validation
Compare analytical model vs. queuing network simulator vs. prototype (mininet emulation).
Under various system loads (i.e. publication rates):
  Under-loaded
  Saturated
  Overloaded
Analytical model for lowest priority class is slightly less accurate, which is normal as these models are approximations.
* Highest priority

## Slide 55: Approach Evaluation
With an overloaded system, switch buffers fill up and cause high delay / packet drops.
Our approach delivers more high priority events than finite buffers only.
High priority events also delivered quicker.
Addition of drop rate policy smooths success rate while reducing end-to-end delay.

## Slide 56: Scalability

## Slide 57: Algorithms Comparison
Prioritization algorithms
  Our bandwidth-aware greedy strategy performs better than bandwidth-unaware version.
  Both better than no prioritization.
  But random priorities are worst: need to set priorities correctly!
Drop rate algorithms
  Convex optimization performs best.
  Compared it with policies that set the drop rates by assigned priority (i.e. linearly or exponentially proportional to priority level).
  Plot shows varying utilities of async events vs. data telemetry: simpler policies perform closer to optimal for larger differences.

## Slide 58: Conclusions & Future Work
Our application-aware prioritization algorithm improves the value of exchanged information by 36% when compared with no prioritization.
Network-aware drop rate policies improve this performance by 42% over priorities only and by 94% over no prioritization.
Prototype implementation validates efficacy of our approach and accuracy of our model in an emulated network setting.
Unified queueing theory framework enables many extensions to our model:
  Priority + drop rate in same algorithm.
  Clustering-based prioritization algs.
  Alternative utility functions.
  Tuning the entire broker network.
  Multiple network interfaces/routes.
  Relaxing assumption of one packet/event used in our analysis (e.g. by using queueing theory “batch arrivals”).
  Packet retransmissions (“closed” queueing network).
  Enforcing priorities in DX broker instead of network switch.

## Slide 59: Thesis Conclusion
Resilient Communications Middleware for IoT Data Exchange
Reduced downtime via overlay monitoring & edge fail-over
Increased value of information captured via event prioritization
Network & Application-awareness
Geo-aware overlays for improved cloud data collection
SDN & Edge Computing
Improved local alerting via redundant multicast
Notes: 1) improve cloud collection
2) ensures downtime of no more than...
3) improves edge alert delivery by....
4) firedex conclusion

## Slide 60: Proposed Middleware Architecture
IoT Devices
IoT DX Middleware
Geo-diverse multi-path
Routing (GeoCRON)
Building Management System Interface
Seismic “pick”
Resilient Overlay Networks
Cloud Services
Analytics
Edge Services
Backup analytics
Resilient alert
Producers
Prioritized subscription
Ride
data collection
Differen-tiated info flow
Local Data Exchange
IoT data
Consumers
Resilient alert subscription
FireDeX
BW Allocation
Prioritization
Ride
Diverse multicast
Is
cloud
up?
Yes
No
SDN
Ride overlay probe
Notes: ----- Meeting Notes (10/26/18 15:31) -----
maybe a slide that just lists each of the contributions
edge network approach to resilient iot data exchange
ideas:
1) improve cloud collection
2) ensures downtime of no more than...
3) improves edge alert delivery by....
4) firedex conclusion

## Slide 61: Future Research Directions
Protocol interoperability
Distributed data exchange brokers
Synchronizing edge and cloud services
Managing mobile IoT devices (esp. in SDN)
Resilient SDN controller placement
Exploiting data semantics for…

## Slide 62: My Next Step
Research Engineer at Real-Time Innovations (RTI) (start Jan. 2019)
E.g. semantic data compression, Layer 7 switching, TSN…

## Slide 63: Acknowledgements
Sponsorship / fellowship awards: Bren ICS, NSF, ARCS foundation, La Verne Noyes fellowship
Various co-authors, esp. Qing Han (GeoCRON), Guoxi Wang (Ride), Georgios Bouloukakis & Luca Scalzotto (FireDeX)
SCALE team, esp. Dan Hoffman / Montgomery Co., Guoxi Wang, and Qiuxi Zhu
CSN team
NIST/NFPA esp. Casey Grant
My dissertation committee
Friends & family