## Slide 1: Spatiotemporal Scheduling for Crowd Augmented Urban Sensing
Qiuxi Zhu, Md Yusuf Sarwar Uddin, Nalini Venkatasubramanian – Univ. California, Irvine, U.S.A.
Cheng-Hsin Hsu – National Tsing Hua Univ., Taiwan
Funded by –
CNS-1450768
MSE 446677-22553

## Slide 2: Motivation
IoT helps achieve fine-grained urban sensing and monitoring
  Environmental phenomena and human activities
  In-situ and mobile devices
  Diverse sensing capabilities
We anticipate that a large number of devices will participate in such activities in the near future.
Redundant data may lead to
  Higher energy cost
  Waste of network and cloud resources
  Little contribution to accuracy
Notes: In-situ: Deployed nodes on street lamps, signal lights, etc.
Mobile: (1) Deployed nodes on buses; (2) Crowd-owned mobile devices.
The large amount of participants and devices can generate a large amount of redundant data, if we do not coordinate them carefully.
Example: Air quality, noise, trash, temperature, wireless network signal strength, etc.

## Slide 3: Spatiotemporal scheduling
Make plans for devices to regulate their sensing behavior (i.e. activate/deactivate their sensors)
  Acceptable space-time coverage with limited data budget
  Reduced redundancy
Challenges
  Device heterogeneity: Availability of multiple sensor types
  Data heterogeneity: Varying spatiotemporal requirements
  Crowd mobility
  Scalability: Number of devices and size of maps
Applicable to other geo-correlated data generation apps
Notes: In IoT systems, it is common that multiple types of sensors coexist on the same device.
These sensors may serve common or different IoT applications.

## Slide 4: Related work
Urban crowd-sensing
  S. Hachem (PerCom ‘13)
  Y. Han (SECON ‘15)
  A. Khan (PMC, 2015)
  Y. Chen (NetGames ‘17)
  M. Talasila (MobiCASE ‘14)
  TRAC (INFOCOM ‘14), etc.
IoT and edge computing
  SCALE2 (SMARTCOMP ‘16)
  H. Hong (CloudCom ‘17)
Pollution monitoring
  A. Marjovi (DCOSS ‘15)
  D. Hasenfratz (PerCom ‘14)
  Y. Zheng (UbiComp ‘14), etc.
Pollution severity
  R. Beelen, ’14
  J. Zhang, ’14
  N. Kunzli, ‘00
  R. T. Burnett, ’00
  X. Xu, ‘94
Notes: Urban crowd-sensing
S. Hachem (PerCom ‘13): Probabilistic registration
Y. Han (SECON ‘15): Utility-maximizing data collection in crowd sensing
A. Kahn (PMC, 2015): A novel localization and coverage framework for real-time participatory urban monitoring
Y. Cheng (NetGames ‘17): Gamifying mobile application for smartphone augmented infrastructure sensing
M. Talasila (MobiCASE ‘14): Alien vs. mobile user game: Fast and efficient area coverage in crowd-sensing
TRAC (INFOCOM ‘14): TRAC: Truthful auction for location-aware collaborative sensing in mobile crowdsourcing
Pollution monitoring
A. Marjovi (DCOSS ‘15): High resolution air pollution maps in urban environments using mobile sensor networks
D. Hasenfratz (PerCom ‘14): Pushing the spatio-temporal resolution limit of urban air pollution maps
Y. Zheng (UbiComp ‘14): Diagnosing New York City’s noises with ubiquitous data
IoT and edge computing
SCALE2 (SMARTCOMP ‘16)
H. Hong (CloudCom ‘17): Supporting internet-of-things analytics in a fog computing platform

## Slide 5: Online scheduling approach
Devices report on-board sensing capability info to server.
Server collects or estimates the location of participating devices.
Server creates the plan which specifies what sensors should be active on which devices now.
Devices activate or deactivate sensors.
This is a device

## Slide 6: Spatiotemporal scheduling
Problem formulation
  Assumptions
  Terms and notations
  Spatiotemporal scheduling as multi-objective optimization
Online scheduling algorithms
Prototype platform and measurements
Performance evaluation and simulation results

## Slide 7: Problem formulation
Cell
Distance between cells is represented in matrix
Distance
Discretize space into cells and time into time frames

## Slide 8: Problem formulation
Data type
Priority
Sensor for
Data rate
Simplicity: Data are generate at constant rate
Communication error and delay are not considered

## Slide 9: Problem formulation
Node
Sensor for
Sensor presence binary matrix
iff is present on

## Slide 10: Problem formulation
Node placement bin. matrix
iff is in at time
Cell
Node
No control on the mobility of mobile nodes

## Slide 11: Problem formulation
Cell
Node
Activation plan bin. matrix
iff is active on at time
Sensor for
Activation state represented by

## Slide 12: Problem formulation
Node is active if any sensor on it is active; it is inactive if no sensor is active
Node
Node is active if any sensor on it is active; it is inactive if no sensor is active

## Slide 13: Problem formulation
Cell
Node
Spatial impact of data type defined by impact function
Temporal impact of data type defined by impact function

## Slide 14: Performance model
Benefits
  Utility: Quality of data collected in each cell in each frame
  Coverage: Probability a cell is covered by some valid data
Cost
  Number of active nodes: Activation overhead
Constraints
  Data quota: Average data generation rate
  Sensor presence: Only existing sensor can be activated
Multi-objective optimization with constraints
Notes: Introduce the favorable decisions here –
We want our collected data be distributed in space and time more uniformly, though some regions could be more densely populated
Coverage: We want to cover more space and time
Utility: If possible, we also want to improve the quality/quantity of data we collect in each cell and time frame
Activation overhead: Human intervention and energy cost to keep device “awake”, etc.

## Slide 15: Benefit: Utility
Utility measures the quality of sensor data.
The utility function is application dependent, but satisfies our assumptions and certain properties, e.g.
  A set of sensors > any subset of these sensors
  Many sensors ≤ sum of each sensor
  Many sensors in one cell < same number but in many cells
Overall utility (i.e. spatiotemporal average)

## Slide 16: Benefit: Coverage
Coverage is the probability that a cell is covered by valid sensor data, considering temporal impact (of historical data points) and spatial impact (of remote data points).
Single-cell single-frame coverage
Single-cell effective coverage (i.e. impacted coverage)
Spatial average coverage at time frame
Average coverage over time frames to
Overall coverage (i.e. spatiotemporal average)

## Slide 17: Cost: Number of active nodes
Number of active nodes captures the activation overhead (e.g. human intervention, energy consumption) of nodes. It is consistent with our assumption that
  Many active sensors on one device > on many devices
Average number of active nodes (i.e. temporal average)

## Slide 18: Constraint: Data quota
An application dependent quota on average data rate
Overall data generation rate (i.e. temporal average)
The data quota constraint is that .
Note that
  The unit of data rate and data quota is byte/sec;
  The constraint applies to the overall data generation rate, not the per-frame data generation rate.

## Slide 19: Multi-objective optimization
Given inputs
  Presence of sensors on nodes, i.e. matrix
  Placement of nodes, i.e. matrix
Find: Plan matrix for each time frame
Optimize
  Overall coverage and overall utility (maximize)
  Average cost (minimize)
Subject to
  Presence constraint
  Data constraint
NP-hardness

## Slide 20: Spatiotemporal scheduling
Problem formulation
  Assumptions
  Terms and notations
  Spatiotemporal scheduling as multi-objective optimization
Online scheduling algorithms
Prototype platform and measurements
Performance evaluation and simulation results

## Slide 21: Naïve: Activating everything
For the given set of trajectories or locations, and the given sensing capacity of nodes, activating everything gives
  Maximum possible coverage
  Maximum possible utility
  Maximum possible number of active nodes (cost)
  Meanwhile, it has
Unbounded data generation (constraint violation), hence not a valid solution when there is a data quota
Benefit objectives (i.e. coverage and utility) of this naïve approach can be used as baselines to compare with those of other algorithms, i.e. check how well they perform.

## Slide 22: Naïve: “Random” (utility first)
Fill up the assigned data budget using a subset of sensors (i.e. node-type pairs)
  Pick the sensors that give higher utility
  Random tie breaking
A quick and valid solution when there is a data quota with certain aspects ignored
  Spatiotemporal requirements of different data types
  Cost of node activation
Unused data budget rolls over to the next time frame.
Notes: The actually naïve approach is to make completely random selections, which is obviously bad.

## Slide 23: Highest score first
Get higher overall performance using assigned data budget
Score of a sensor (i.e. a node-type pair) is defined as the performance gain divided by data consumption, i.e.
Select the node-sensor pair with the highest score, add it to the plan, and loop until: (1) All sensors are active, (2) Data quota is used up, or (3) Highest score is non-positive.
Any selection could affect scores of unselected sensors.
Unused data budget rolls over to the next time frame.
Notes: Recall that the overall performance includes three terms: Utility, coverage, and node activation.
Time complexity: O(K * M ^ 2 * N + K * M * N ^ 2 + K ^ 2 * N ^ 2)

## Slide 24: Highest score first
Start with an empty
For every node-sensor pair that is not marked as active and does not violate data quota constraint in , compute its score
Mark the pair with highest positive score as active, and loop until…
Slow termination: When highest score is negative
Unit-data performance gain, i.e.
Notes: There are 3 (three) ways this algorithm terminates:
All sensors are active
Data quota runs out
Highest score is non-positive

## Slide 25: Lyapunov control
Match used data (actually generated) with data quota
State of the system is represented by a “queue”, the size of the queue is the total amount of data generated up to the current time frame, i.e. .
Lyapunov function
Lyapunov drift
Minimizing “drift minus reward” is equivalent to maximizing
Notes: Lyapunov control allows us to over-draft data budget from future time frames when there is a good opportunity in the current one.
This is actually another way to define the “score” to use in HSF

## Slide 26: SCALECycle platform
Donald Bren Hall
Thingstitute
IoT Lab
Victory Court Senior Apartments
Good
Poor
Montgomery County, MD
“MCGUEST”
University of California, Irvine
“UCInet Mobile Access”
Notes: SCALE multi-sensor boxes on bikes or in backpack.
Prototype: (1) Raspberry Pi Model B; (2) USB battery pack; (3) Bluetooth GPS; (4) Wi-Fi adaptor; (5) Air quality (TGS 2600)
Can be extended to support multiple types of sensors and networks.

## Slide 27: SCALECycle architecture

## Slide 28: Initial measurements
Sensors (NTHU testbed)
  Gas sensors: MQ-5, MQ-7, MQ-131, MQ-135
  Microphone: Adafruit 3367 USB Microphone
  Camera: RPi Camera Module
  GPS: Globalsat BU-353S4 GPS Reader
Sensors (UCI-Montgomery testbed)
  Air contaminant: TGS2600
  GPS: HP iPAQ Bluetooth GPS System
  Wi-Fi dongle: Edimax
Initial measurements stored locally on the SD card

## Slide 29: Initial measurements
Montgomery County, MD
NTHU Campus, Hsinchu City, Taiwan
Sensor type | Format | Sampling pattern | Sample
Analog sensors | JSON text | 1 message every 5 sec | 200 B
Microphone | WAV | 1 clip of 8 sec every minute | 800 KB
Camera | JPG | 1 picture every 20 sec | 180 KB
Wi-Fi iwlist | JSON text | 1 list of 20 items every 4 sec | 3600 B

## Slide 30: Performance evaluation
Simulation framework written in R (https://www.r-project.org/)
Mobility traces generated by the ONE Simulator (https://akeranen.github.io/the-one/) based on the built-in Helsinki map – size , and pedestrian mobility – speed .
For each time frame, the simulator
  Computes the placement of nodes for the time frame;
  Runs the planning algorithm;
  Applies the plan and computes the objectives.
Sensor types and data generation rates are driven by measurement study.

## Slide 31: Simulation setup
Num. of nodes or
Num. of mobile nodes
Num. of cells ()
Size of cells
Num. of data types
Length of time frame
Length of simulation
Data quota
Coefficients
Type | r (B/s) | Wt. | S. Imp. | T. Imp.
G1 | 40 | 8 | 550 | 20
G2 | 40 | 5 | 550 | 20
G3 | 40 | 5 | 550 | 20
G4 | 40 | 4 | 550 | 20
G5 | 40 | 4 | 550 | 20
G6 | 40 | 3 | 550 | 20
A7 | 107 K | 5 | 100 | 5
P8 | 9,000 | 7 | 10 | 60
P9 | 9,000 | 6 | 750 | 30
W10 | 900 | 3 | 20 | 60
Distance coefficient of exp. decrease func.
Time before step-down

## Slide 32: Performance evaluation
Simulation
  UCI ICS OpenLab Cluster
  2x Quad-core Intel Xeon 3.0GHz CPU E5450 CPU
  32 GB RAM
  CentOS 7.3 (64-bit), Linux 3.10.0-327.22.2.el7.x86_64
  R 3.3.2 (64-bit)
  The ONE Simulator d7fe68e (2017-01)
Metrics
  Overall performance
  Individual objectives
  Quota utilization
  Algorithm running time
Algorithms compared
  Everything (naïve)
  Random (utility first)
  HSF—ST
  Lyapunov control
  Genetic algorithm

## Slide 33: Results
Node mobility
Fixed total # nodes: 50
Varying # mobile: 0~50
Varying speed: 10~200%
Mobile nodes (↑) → Performance (↑)
Close-to-best performance
30% fewer active nodes
Speed (↑) → Performance (↑)

## Slide 34: Results
Device heterogeneity
Fixed total # sensors, all mobile
Uniform dist. sensors on nodes
Varying # nodes: 50~200
Lyapunov performs better as sensors are dist. (↑) sparsely
Notes: As sensors are distributed more sparsely over the increasing number of nodes:
It is more costly to achieve same coverage
Lyapunov performs better in terms that it balances the benefits vs. cost tradeoff better

## Slide 35: Results
Scalability
Varying # nodes: 5~200
Fixed total # nodes: 100
Varying quota: 64 KB~8 MB

## Slide 36: Conclusion
Contributions
  Motivated and formalized the spatiotemporal scheduling problem for crowd-augmented urban sensing;
  Proposed an online framework and two algorithms;
  Conducted measurement-driven simulations showing the effectiveness of proposed approach.
Achieved similar coverage (comparing to “everything”) under data constraints, with about 30% fewer active nodes.
Future works
  Improve scalability with scheduling hierarchies
  Study impact of network connectivity and uncertainty

## Slide 37: Questions?
Distributed Systems Middleware (DSM) Group at UCI http://www.ics.uci.edu/~dsm/
Information Systems Group (ISG) at UCI https://isg.ics.uci.edu/
Networking and Multimedia Systems Lab (NMSL) at NTHU https://nmsl.cs.nthu.edu.tw/
Safe Community Awareness and Alerting (SCALE) Project http://scale.ics.uci.edu/
Qiuxi Zhu https://sites.google.com/site/zhuqiuxiuci

## Slide 38: Spatiotemporal Scheduling for Crowd Augmented Urban Sensing
Thank you!
Email: qiuxiz <at> ics <dot> uci <dot> edu
Funded by –
CNS-1450768
MSE 446677-22553